## Slide 1: Building Energy Overview

## Slide 3: How Much is 100 quads?

## Slide 6: Current Use and Projections (quads)
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Propane | 0.04628 | 0.046362 | 0.045592 | 0.045361 | 0.041823 | 0.041267 | 0.040548 | 0.039788 | 0.039063 | 0.038406 | 0.037764 | 0.037163 | 0.036597 | 0.03608 | 0.035558 | 0.035062 | 0.034581 | 0.034136 | 0.03371 | 0.033317 | 0.032942 | 0.032553 | 0.032184 | 0.031807 | 0.031461 | 0.031123 | 0.030815 | 0.030528 | 0.03025 | 0.029981
Kerosene | 0.00684 | 0.002115 | 0.001991 | 0.001989 | 0.001674 | 0.001583 | 0.001527 | 0.001495 | 0.001457 | 0.001419 | 0.001379 | 0.001342 | 0.001306 | 0.001271 | 0.001239 | 0.001208 | 0.001179 | 0.001151 | 0.001123 | 0.001097 | 0.001071 | 0.001044 | 0.001019 | 0.000994 | 0.000971 | 0.000948 | 0.000926 | 0.000905 | 0.000883 | 0.000863
Petroleum Liquids | 0.26812 | 0.25568 | 0.27568 | 0.27375 | 0.24798 | 0.24398 | 0.2394 | 0.23438 | 0.2289 | 0.22343 | 0.21802 | 0.21288 | 0.20795 | 0.20336 | 0.19878 | 0.1944 | 0.19003 | 0.18585 | 0.18171 | 0.17777 | 0.17399 | 0.17025 | 0.16669 | 0.16323 | 0.15999 | 0.15685 | 0.1539 | 0.15108 | 0.14836 | 0.14572
Natural Gas | 0.85195 | 0.75341 | 0.88975 | 0.8988 | 0.84397 | 0.84348 | 0.84296 | 0.84086 | 0.83787 | 0.83525 | 0.83115 | 0.82695 | 0.8228 | 0.81849 | 0.81318 | 0.80791 | 0.80236 | 0.79701 | 0.7912 | 0.78571 | 0.78203 | 0.78054 | 0.77891 | 0.77605 | 0.77207 | 0.76717 | 0.76219 | 0.75749 | 0.75185 | 0.74547
Renewable Energy | 0.054241 | 0.048191 | 0.061914 | 0.060989 | 0.054682 | 0.053382 | 0.052412 | 0.051844 | 0.051647 | 0.051625 | 0.051608 | 0.051603 | 0.051559 | 0.051505 | 0.051402 | 0.051247 | 0.051089 | 0.050894 | 0.050677 | 0.050444 | 0.050234 | 0.050026 | 0.049863 | 0.049726 | 0.049532 | 0.049288 | 0.049049 | 0.048817 | 0.048623 | 0.048463
Electricity | 0.4621 | 0.44644 | 0.45151 | 0.43546 | 0.44074 | 0.43974 | 0.44078 | 0.44152 | 0.44136 | 0.43572 | 0.43442 | 0.43513 | 0.43653 | 0.43704 | 0.43641 | 0.43657 | 0.43699 | 0.43802 | 0.43894 | 0.43866 | 0.43848 | 0.43934 | 0.44127 | 0.44298 | 0.44431 | 0.4454 | 0.44614 | 0.4472 | 0.44824 | 0.44909

## Slide 7: Current Use and Projections
Delivered energy consumption in residential sector is projected to decrease by 15% by 2040 due to improvements in the efficiency of household appliances and heating systems and improvements in the envelope
To achieve the 80% GHG reductions called for in New York, housing energy use needs to be reduced by 35% to 60% over current levels

## Slide 8: Current Use and Projections

## Slide 9: Current Use and Projections
Chart: 
| Natural Gas | Electricity | Petroleum Liquids | Renewable Energy | Propane | Kerosene
2011 | 0.85195 | 0.4621 | 0.26812 | 0.054241 | 0.04628 | 0.00684

## Slide 10: Current Use and Projections
Chart: 
| Natural Gas | Electricity | Petroleum Liquids | Renewable Energy | Propane | Kerosene
2040 | 0.74547 | 0.44909 | 0.14572 | 0.048463 | 0.029981 | 0.000863

## Slide 11: Electricity in New York
Chart: Percent of Electricity Produced in NY
| 1990 | 2000 | 2010
Petroleum | 0.25036 | 0.10824 | 0.014639
Natural Gas | 0.1679 | 0.28772 | 0.35715
Coal | 0.19146 | 0.18113 | 0.099172
Hydroelectric | 0.20048 | 0.17323 | 0.18211
Nuclear | 0.17454 | 0.22819 | 0.3057
Other Renewables | 0.014607 | 0.020874 | 0.035153
Other | 0.00065783 | 0.00062429 | 0.0060736

## Slide 12: Direct CO2 Emissions (million MT)
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Petroleum | 19.2326 | 18.3218 | 19.678 | 19.5391 | 17.6918 | 17.4058 | 17.0781 | 16.7194 | 16.3257 | 15.9329 | 15.5441 | 15.1743 | 14.82 | 14.4899 | 14.1603 | 13.8454 | 13.5305 | 13.2298 | 12.9318 | 12.6472 | 12.3752 | 12.1058 | 11.849 | 11.6003 | 11.3667 | 11.1406 | 10.928 | 10.7251 | 10.529 | 10.3391
NaturalGas | 45.0779 | 39.9749 | 47.207 | 47.687 | 44.7784 | 44.7522 | 44.7247 | 44.6134 | 44.4546 | 44.3155 | 44.098 | 43.8752 | 43.6552 | 43.4263 | 43.1444 | 42.865 | 42.5708 | 42.2865 | 41.9785 | 41.6871 | 41.4919 | 41.4129 | 41.3264 | 41.1746 | 40.9634 | 40.7034 | 40.4392 | 40.1901 | 39.8906 | 39.5523
Electricity | 62.6 | 58.0269 | 62.525 | 55.5712 | 55.757 | 55.7968 | 55.8772 | 56.6737 | 56.8116 | 55.8756 | 55.3197 | 54.7216 | 54.2033 | 53.889 | 53.2405 | 52.6912 | 51.3931 | 50.4501 | 50.2192 | 49.344 | 50.1553 | 51.7338 | 52.8123 | 53.2098 | 53.5871 | 53.7831 | 53.7409 | 53.7675 | 53.4328 | 52.5843

## Slide 13: Projections for Direct CO2 Emissions
Direct CO2 emissions from the residential sector are projected to decrease by 19% by 2040 due to improvements in building efficiency and greening of the electricity grid
This can be compared to the 80% GHG reductions called for in New York which which is already unlikely to be sufficient

## Slide 14: Opportunities for Efficiency Improvements Abound

## Slide 17: Current Use and Projections
Chart: 
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040
Delivered Energy | 1.6364 | 1.5037 | 1.6789 | 1.669 | 1.5874 | 1.5806 | 1.5756 | 1.5686 | 1.5598 | 1.546 | 1.5352 | 1.5266 | 1.5188 | 1.5104 | 1.4998 | 1.4901 | 1.4805 | 1.4718 | 1.4625 | 1.4526 | 1.4447 | 1.4402 | 1.4367 | 1.432 | 1.4259 | 1.4187 | 1.4113 | 1.4046 | 1.3971 | 1.3887
Electricity Related Losses | 1.1218 | 1.0974 | 1.1233 | 1.0429 | 1.0324 | 1.0427 | 1.0552 | 1.0609 | 1.0564 | 1.0213 | 1.0032 | 0.98777 | 0.98725 | 0.98013 | 0.96969 | 0.95858 | 0.9324 | 0.91487 | 0.91091 | 0.89468 | 0.91132 | 0.94132 | 0.9603 | 0.96651 | 0.97279 | 0.97635 | 0.97613 | 0.97624 | 0.97026 | 0.95555

## Slide 18: Opportunities for Efficiency Improvements Abound

## Slide 19: Opportunities for Efficiency Improvements Abound
Chart: Solar PV Installed per Year (kW)
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Installed PV | 5.3 | 7.2 | 4 | 5 | 4.2 | 13.6 | 4.2 | 21.6 | 32.8 | 57 | 88.4 | 272.8
Price per Watt | 8.06 | 8.24 | 10.3 | 8.77 | 8.38 | 8.68 | 7 | 6.82 | 5.37 | 5.45 | 4.45 | 4

## Slide 20: Opportunities for Efficiency Improvements Abound
Chart: Solar PV Installed per Year (kW)
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
Tompkins County | 57.6 | 18.6 | 74.1 | 135 | 102.9 | 110.4 | 78.4 | 121 | 186 | 237.9 | 748.2 | 2516
Cortland County | 5.3 | 7.2 | 4 | 5 | 4.2 | 13.6 | 4.2 | 21.6 | 32.8 | 57 | 88.4 | 272.8

## Slide 21: We Will Focus in this Class on Space and Water Heating

## Slide 22: How Energy is Used in the Home

## Slide 23: How Energy is Used in the Home

## Slide 24: How Energy is Used in the Home

## Slide 25: How Energy is Used in the Home

## Slide 26: When Looking at Data for New York Don’t Forget about “the City”

## Slide 27: Despite Cold Climate NY is Not Far Ahead in Higher Efficiency Heating Systems

## Slide 28: How Energy is “Lost” / Wasted in the Home

## Slide 29: How Energy is “Lost” in the Home Improper or Inadequate Insulation

## Slide 35: The Center for Energy Efficient Design (CEED)
Located in Franklin County, Va.
Built in 2009-10
The first US public school designed to the Passivhaus building standard.
Cost premium of 3.1% with 7 year payback
Annual energy savings = $3,450

## Slide 36: Family Run Dental Clinic
Located in Roanoke, Va.
5,400 sq ft built in 2011-13
Built for $155 / ft2 compared to typical conventional dental clinic costs of $150 to $200 / ft2
Uses 70% less energy than conventional construction
Annual energy savings of $9,300

## Slide 37: Malcolm Rosenberg Hillel Center for Jewish Life
Located in Blackburg, Va across from Virginia Tech
8,000 sq ft built in 2011-13
First Passivhaus building with commercial kitchen inside
Built for $135 / ft2
Uses 60% less energy than conventional construction

## Slide 38: Hickory Hall - Emory & Henry College
Located in Emory, Va.
Built in 2012-13
Largest Passivhaus building in US.
Uses 62% less energy than its twin Elm Hall which is LEED certified and 74% less than code
Employs GSHPs and energy recovery vehicles
Reduced installed cooling capacity from 68 tons in Elm Hall to 14 tons and reduced heating capacity from 68 tons to 12 tons even though it is 11% larger than Elm Hall

## Slide 39: Hickory Hall - Emory & Henry College
Hickory Hall (40,000 sq ft and 117 beds) = $118.25 / ft2
  Completed in 2013
Elm Hall (36,000 sq ft and 116 beds) = $125 / ft2
Completed in 2010

## Slide 40: Passivehaus Kindergarten in Germany

## Slide 41: Oversized Boilers and Furnaces

## Slide 42: Outdated Distribution Systems

## Slide 45: High Efficiency Heating

## Slide 46: Ground Source Heat Pumps (GSHP)
Uses familiar refrigeration technology
Super efficient way to use electricity for 100% of building heating and cooling for all size buildings
Efficiencies of up to 300% by extracting heat from the ground
Notes: No shortage electricity supply
Heat produced at normal building heating temperatures

## Slide 47: Professional Studies Building SUNY Cortland

## Slide 48: Professional Studies Building 40 wells and approximately 35 tons of capacity
Notes: These wells contain roughly 35 gallons of glycol in total

## Slide 49: Professional Studies Building – Heat Pump

## Slide 50: Professional Studies Building – Heat Pump

## Slide 51: Professional Studies Building – Heat Pump

## Slide 52: Air Source Heat Pumps (ASHP)
Same refrigeration technology as ground source heat pumps
Efficiencies of up to 200% by extracting heat from the air
Remain operational to air temperatures as low as -13 oF
Notes: % efficiency comparison

## Slide 53: Air Source Heat Pumps for DHW
Efficiencies of up to 150-200% by extracting heat from the air
Provide supplemental dehumidification if located in basement
More complex to consider if they have to be located within the thermal envelope
Notes: % efficiency comparison

## Slide 54: When Electrifying the Heating System we Need to Consider the Source of the Electricity

## Slide 55: Electricity in New York
Chart: 
| Natural Gas | Nuclear | Hydroelectric | Coal | Wind | Biomass | Petroleum | Other | Solar
 | 54354386.61 | 44755606 | 24530421.28 | 4697104.74 | 3539498 | 2281595.41 | 1007373.31 | 883827.46 | 67017.16

## Slide 56: Greenhouse Gas Emissions from Heating
Greenhouse gas emissions reduced by 45 to 65 % if using heat pumps powered by grid electricity

## Slide 57: Greenhouse Gas Emissions from Heating
Greenhouse gas emissions reduced by more than 97 % if using heat pumps powered by solar PV